## Slide 1: ADMINISTRATION BUILDING
Justin Purcell
Structural Option
Advisor: Dr. Hanagan

## Slide 2: PRESENTATION OUTLINE
Building Background
Existing Structural System
Proposal
Proposed Structural System
Cost and Schedule Analysis
Electrical Redesign
Conclusions
Questions and Comments

## Slide 3: PROJECT BACKGROUND

## Slide 4: BUILDING INFORMATION
Owner: Confidential Client
Location: Pennsylvania
Building Type: Office and Specialty Amenity Spaces
Size: 311,905 S.F.
Stories: 5/4 Above Grade
F-F Height: 20’ For Ground Floor, 13.33’ For Floors 1-5
Building Height: 87’
Construction Dates: 10/22/01-7/24/03

## Slide 5: KEY PLAYERS
Architect: KlingStubbins
CM: Skanska
Engineer: KlingStubbins

## Slide 6: EXISTING STRUCTURAL SYSTEM

## Slide 7: GRAVITY SYSTEM
  3 ¼” Lightweight Concrete Slab,
  4,000 PSI Concrete Strength
  3” Composite Metal Deck
  W18x35 Composite Beams-40’
  W18x35 Composite Girders-20’
  W12x96 Columns-13.33’

## Slide 8: GRAVITY DESIGN LOADS
LIVE LOAD | 
FLOOR: | 100 PSF
ROOF: | 150 PSF
FLOOR DEAD LOAD | 
CONCRETE SLAB: | 35 PSF
SUPERIMPOSED: | 30 PSF
STEEL STRUCTURE | 15 PSF
EXTERIOR BRICK TRUSS PANEL | 40 PSF

## Slide 9: TYPICAL FLOOR

## Slide 10: LATERAL SYSTEM
  Braced Frames (Frames in Red)
  HSS 8x6x½ Braces
  Coordinated With Mechanical Distribution

## Slide 11: BRACED FRAMES

## Slide 12: PROPOSAL

## Slide 13: GOALS
  Change Existing Structural System To A One-Way Slab, CIP Concrete System
  Estimate Cost Of Existing And Proposed Structural System
  Estimate Schedule Of Both Systems
  Redesign Electrical System To Limit The Number Of Transformers

## Slide 14: STRUCTURAL REDESIGN

## Slide 15: DESIGN PROCEDURE
ASCE 7-05
ACI 318-02
CRSI 2002 Design Manual
E-TABS
Unit Strip Method
PCA Slab And Column
Hand Calculations

## Slide 16: STRUCTURAL OVERVIEW
6” Normal Weight Concrete Slab-CIP
16” x 28” CIP Beams
20” x 26” CIP Girders
20” x 30” CIP Columns
Moment Frames
Design Floor And Roof Loads:
DESIGN LIVE LOAD | 
FLOOR LOAD: | 100 PSF
ROOF LOAD: | 150 PSF
DESIGN DEAD LOAD | 
CONCRETE SLAB: | 88 PSF
SUPERIMPOSED: | 30 PSF

## Slide 17: TYPICAL FLOOR

## Slide 18: SLAB DESIGN
  4000 PSI Concrete, 60 KSI Steel Reinforcing
  Minimum 5” Thick Concrete Slab Based On ACI
  6” Thick Concrete Slab Was Used
  Pattern Loading Considered To Find Critical Moments
  Steel Reinforcing
    Bottom: #3’s @ 8” O/C (Positive)
    Top: #4’s @ 12” O/C (Negative)
    T-S: #4’s @ 15” O/C

## Slide 19: COLUMN DESIGN
Designed For 1300 Kips and 750 K-FT
Gravity and Lateral Loads
Slenderness Considered Based On ACI For Lateral Loads
4000 PSI Concrete
# 3 Ties

## Slide 20: COLUMN DESIGN
20” x 30” CIP Column
32 #10 Bars
Oriented So That The 30” Depth Handles The Larger Wind Force In The Long Direction

## Slide 21: BEAM DESIGN
Moment and Shear Coefficient Analysis
16” x 28” Beam
Steel Reinforcing
  Bottom: 2 #11’s
  Top: 2 #11’s
  Stirrups: #5’s
L/370 Deflection Ratio

## Slide 22: GIRDER DESIGN
Moment and Shear Coefficient Analysis
20” x 26” Girder
Steel Reinforcing
  Bottom Bars: 3 #11’s
  Top Bars: 4 #14’s
  #5 Stirrups
L/706 Deflection Ratio

## Slide 23: MOMENT FRAMES
Designed To Resist Lateral Loads In Both Directions
Achieved From CIP Monolithic Pour At Every Connection
For Simplicity Of Lateral System And Ease Of Construction, Every Column And Beam Connection Is A Moment Connection
Forces Distributed By Relative Stiffness
32 Moment Frames
  6 In The Short Direction
  26 In The Long Direction

## Slide 24: LATERAL DRIFT
Combination Of Shear Deflection And Bending Deflection
Controlled By Wind
Drift Found To Be Less
Than 1” In Both Directions
  0.2” In Long Direction
  0.15” In Short Direction

## Slide 25: ADVANTAGES OVER EXISTING STRUCTURAL SYSTEM
Floor Depth Savings: 5”
Beam Deflection Savings: 0.7”
Girder Deflection Savings: 0.4”
# Of Column Savings: 76
Drift Savings: 0.37”

## Slide 26: COST AND SCHEDULING

## Slide 27: EXISTING STRUCTURAL SYSTEM
Cost Estimate #1: $8.62 Million
  Estimate Based On G.C.’s Suggestions And Feedback
Cost Estimate #2: $7.71 Million
  Estimate Based On R.S. Means 2008
  Detailed Estimate Based On Takeoff Per L.F. Of Steel
Cost Estimate #3: $8.67 Million
  Estimate Based On R.S. Means 2008
  Generic Steel Estimate Based On A 3-6 Story Steel Building

## Slide 28: EXISTING STRUCTURAL SYSTEM
Schedule For Estimate #1: N/A
Schedule For Estimate #2: 5 Months
Schedule For Estimate #3: 5 Months

## Slide 29: PROPOSED STRUCTURAL SYSTEM
Cost Estimate #1: $13.46 Million
  Based On R.S. Means 2008
  Detailed Estimate Based On Takeoff
Cost Estimate #2: $12.44 Million
  Based On R.S. Means 2008
  Generic Estimate Based On CIP One-Way Slab W/Beams and Columns

## Slide 30: PROPOSED STRUCTURAL SYSTEM
Schedule For Estimate #1: 15 Months
Schedule For Estimate #2: 15 Months

## Slide 31: ELECTRICAL DESIGN

## Slide 32: PROBLEM STATEMENT
There Is An Excessive Amount Of Transformers
Currently There Are 50 Transformers
GOALS:
  Reduce Number Of Transformers
  Resize The Feeders

## Slide 33: PROBLEM STATEMENT

## Slide 34: PROBLEM STATEMENT

## Slide 35: SOLUTION EXAMPLE
BEFORE:
AFTER:

## Slide 36: SOLUTION EXAMPLE
LEFT SIDE:
  Transformer Savings: 5
  Connected Load: 53 KVA-Telecommunications
  Replaced With 75 KVA Eaton 480V-208/120V
  Replaced Feeder With 2 Sets Of 4 KcMil Wire

## Slide 37: SOLUTION EXAMPLE
RIGHT SIDE:
  Transformer Savings: 3
  Connected Load: 35 KVA-Telecommunications
  Replaced With 45 KVA Eaton 480V-208/120V
  Replaced Feeder With 2 Sets Of 4 KcMil Wire

## Slide 38: REDESIGN OVERVIEW
Transformers Before: 50
Transformers After: 11
Savings: 39
Utilized Eaton 480V-208/120V Transformers

## Slide 39: RECOMMENDATION AND CONCLUSIONS

## Slide 40: RECOMMENDATION
Keep Structural System As Steel Composite System With Braced Frames For The Following Reasons:
  Cost
  Erection Time

## Slide 41: CONCLUSIONS
Initial Cost Analysis Was Proven Wrong
Recommend Keeping Existing Structural System
Able To Reduce The Number Of Electrical Transformers

## Slide 42: ACKNOWLEDGEMENTS
KlingStubbins, Especially Bill Gillespie
Dr. Hanagan, Professor Parfitt And The Rest Of The AE Department
Ben Kovach At Balfour Beatty
Pennsylvania State University
Fellow AE’s
My Family And Friends

## Slide 43: QUESTIONS AND COMMENTS