Introduction

Design Criteria and Materials:

*Data Taken from IESNA Handbook

Design Methods:

Lighting Plan

Ramp Results:

Pathway Results:

# Text boxes

- LED striplights uniformly illuminate ramp and draw focus

- Post fixtures lead visitors down the sidewalk and integrate a nautical feel

- Linear fluorescents placed at grazing angles uniformly illuminate the exterior wall without taking away from the sculpture lit from within the atrium

- The wall sconce draws focus towards the entrance

- Bollard fixtures bring focus down to human scale and mark the entrance to the ramps

Location

- Adjacent to Wells Street facing south

Function:

- Serves as main entrance and first impression to the building

Design goals:

- Create flattering first impression

- Create focal points using luminance contrasts

- Clearly define circulation patterns to guide visitors towards entrance

Design concept: Nautical and technological context

- Combine the nautical context of Baltimore and the technological purpose of the building

The post fixtures add a modern, nautical look and provide a uniform illuminance of 5 fc.  This may be a bit high, however, considering the area will be well lit, a higher adaptation level will be required.  The bollards bring focus down to human scale, creating focal points at the beginning of the ramps.  The fluorescent fixtures uniformly illuminate the brick façade without taking attention away from the interior.

*Illuminance scale based on 50 lux

Using the LED strip lights, @ 1.8 lumens each, spaced 2.4” apart, 200 lamps provide an average horizontal illuminance of 5 fc on the brick ramp.  The smooth gradient of light creates a dramatic look while serving as a guide for those visiting the building.

*Illuminance scale based on 100 lux

Wells Street

Tree

Ramp

Vestibule

Brick Paving

Grass

Sculpture

As I have previously described in meeting the needs of the partially sighted, lighting design methods include creating uniform,  linear gradients of illuminance to guide the partially sighted.  In this way, attention will be brought to three-dimensional objects, creating strong contrasts.  On the left are some examples of the look I would like to achieve.

To adapt to the nautical context of Baltimore, lantern-like fixtures will be chosen.  However, I want to stay away from “old fashioned” concepts which would contradict my metaphor of rising technology and advancement for the future.

Finally I want the decorative sculpture to be seen from within.  Overall, floodlighting the building façade will be avoided so the interior can be viewed from the exterior.